## Slide 1: Quality management in the National topographic database of Finland
Ulla Pyysalo, Quality KEN 25.4.2019.

## Slide 2: Background
Project: The new national topographic database of Finland, 2015-2019, phase I
Workpackage; Quality management in the National topographic database of Finland
Group; Ulla Pyysalo, Teppo Ahonen, Jarmo Annunen, Hannu Villman, Antti Federley
Timetable 2019
Previous project NTDB data quality (2015-2016)
    Quality handbook for aerial images and orthophotos
    Quality handbook for laser scanning (3D point clouds)
    Quality handbook for digital elevation model (DEM)
Notes: Syy, miksi esityksen aihe tämä, eikä conceptual models
  Paketti alkanut vuoden vaihteessa
  Sopii ryhmälle
  Kysymyksiä ryhmälle

## Slide 3: national topographic database of Finland, roles
Notes: Consept and roles
Cordinator kerää aineistot, joita muut ylläpitävät
Data producer
Data supplier
NLS kaksoisrooli

## Slide 4: questions
Who is responsible for quality management?
How do we share responsibility?
Can NTDB coordinator give quality promises for data collected by others?
NTDB
Quality requirement
Quality promise
NTDB
NTDB
NTDB
Quality requirement
No quality requirement
No quality requirement
No quality promise
No quality promise
Quality promise
1
Spatial data
Spatial data
Spatial data
Spatial data
2
3
4

## Slide 5
Quality management
24.4.2019
5
Quality assunrance
Quality control
Quality design
Quality improvement
“Management activities and functions involved in determination of quality policy and its implementation through means such as quality planning and quality assurance.”
Notes: Hoe to

## Slide 6: Quality management
Quality assunrance
Quality design
Quality improvement
NTDB coordinator
Data producer
Quality control

## Slide 7: Quality design
“Quality design focuses on setting quality objectives and defining the operational processes and resources needed to achieve quality objectives.”
Done by the NTDB coordinator, ie NLS.
By setting quality the requirements and promises. The requirements are more tight than promises.
Writing Quality handbook for NTBD spatial data 2019.
  Data quality elements
  Quality measures
  Appendix: Quality Requirements and promises
  Appendix: Quality Rules
Quality design

## Slide 8
2019

## Slide 9: Quality control
“Quality control refers to that part of quality management that focuses on meeting quality requirements.”
These include for example
  Work instructions; NTDB coordinator provides conceptual models and formatting instructions.
  Competence, such as knowledge, skills, experience, and qualifications. Each data producer applies quality control in its own organization.
Quality control

## Slide 11: Quality assurance
“Quality assurance is the part of quality management that focuses on giving confidence that quality requirements will be met. This is a practical quality work based on commonly agreed quality work practices and responsibilities.”
Divided between data producers and the NTDB coordinator.
Quality assurance is considered to include
  Quality tests and
  Data producer audits.
Quality assurance

## Slide 12: Quality test
Measurable quality elements
Thematic accuracy
Temporal quality
Positional accuracy
Logical consistency
Completeness
Absolute or external accuracy,
XYZ
Accuracy of a time measurement
Temporal consistency
Temporal validity
Classification correctness
Non-quantitative attribute correctness
quantitative attribute accuracy
Omission
Comissiom
NTDB co-ordinator
Data producer
Conceptual consistency
Domain consistency
Format consistency
Topological consistency
QualityGuard

## Slide 13
“Towards Automating Spatial Data Quality Evaluation in the Finnish National Topographic Database”
SDQ 2018: International Workshop on Spatial Data Quality, Malta, Wednesday 7th February 2018
Nils Mesterton and Riikka Kivekäs, National Land Survey of Finland

## Slide 14: What Shall…
NOT PASS
Invalid and empty geometries
Obligatory attributes
Overlapping buildings and building parts
PASS
Voidable attributes
Most issues regarding topological consistency
”Area in meters must be presented using the numeric data type”.

## Slide 15: Data delivery process
Application
Audit process
Agreement
Data delivery
User license

## Slide 16: Audit process
1. Questionnaire
- Data
- Process
- Quality management
- Commitment
2. Audit meeting
- Facilities: hardware, software
- Human resources
3. Report
- Decision (accepted/not accepted)
- Summary
- Development needs, measure proposals
4. Tracking meeting
- Commitment:
development needs, measure proposals fulfilled?

## Slide 17: NLS Quality assurance
Quality test by a consultant.
Demonstration of requirements specified in the NLS - Ministry of Agriculture and Forestry agreement.
  14 test fields Around Finland
  1x1 km for buildings
  3x3 km for roads and addresses
  Completeness (commission/omission) for buildings and roads
  Thematic accuracy for addresses (Municipalities official addressees compared to addressees in NLS GIS database)
  Field surveys <> data
Quality assurance

## Slide 18: Quality improvement
“Improving quality means systematic harmonization and development of policies.”
  NTDB: QualityGuard reports
  Data producer: responding to the report, data correction.
Quality improvement

## Slide 19: summary
24.4.2019
19
Quality design
Quality requirements
Quality promises
Quality control
Conceptual models
Formatting instructions
Competence, such as knowledge, skills, experience, and qualifications
Quality assurance
Quality test for logical consistency
QualityGuard-reports
Audit process
Quality test for completeness, thematic and positional accuracy
Quality improvement
Responding to the QualityGuard report, data correction.
NTDB coordinator
Data producer

## Slide 20: Thank you for attention